## Slide 1: Cache Design Exploration Simulator
Bernadette Williamson
CS 4200 – Final Project

## Slide 2: Introduction
Goal – simulate how CPU caches store and retrieve memory
Compares different cache designs
  Direct-mapped
  2-way set associative
  4-way set associative
Caches improve performance by reducing memory access time
Different designs impact
  Hit rate
  Miss rate
  Performative efficiency

## Slide 3: Cache Basics
Cache Structure
Memory is divided into blocks
Cache is divided into sets
Each set contains ways
Key Ideas
Hit is data already in cache
Miss is data that must be loaded
Eviction is replacing old data
LRU policy removes least recently used block

## Slide 4: System Overview
What the simulator does:
Reads memory addresses from a hex_inst.txt file
Simulates cache access for direct-mapped, 2-way, and 4-way
Tracks hits, misses, writebacks, evictions

## Slide 5: Code Structure
Main Components
cache_make() – builds cache structure
addr_parts() – computes tag and set index
cache_access() – handles hit/miss logic
choose_victim() – LRU replacement
run_sim() – runs the simulation

## Slide 6: Demonstration of Code

## Slide 7: Observations and Findings
Increasing associativity reduces conflict misses
Direct-mapped cache is most sensitive to collisions
4-way cache performs best for repeated data access
Main Takeaway
Cache performance depends heavily on memory access patterns